## Slide 1: WAVELENGTH ASSIGNMENT IN OPTICAL NETWORKS
By,
Ashish Natani Rajiv Jayant Saurabhi Vadalkar Vijay Sharma
Vinod Vokkarane

## Slide 2: Introduction
Optical networks:
  provide high network capacity
  reduced costs for applications such as Internet, video and multimedia applications
Wavelength division multiplexing (WDM):
  Divides bandwidth of fiber into multiple wavelength channels
  Multiple users can transmit at distinct wavelength channels through the same fiber concurrently.
Networks no longer limited by transmission bandwidth, but by processing capability of electronic switches, routers and multiplexers.

## Slide 3: What is a Light Path?
An optical path established between two nodes
Created by allocation of wavelength throughout the path.
Provides a ‘circuit switched’ interconnection between two nodes.
Desirable to establish light paths between every pair of nodes.
Limitations in WDM routing networks,
  Number of wavelengths is limited.
  Limited number of end-to-end connections.
  Physical constraints:
    limited number of optical transceivers limit the number of channels.

## Slide 4: Wavelength Conversion
Process of converting the wavelength of an incoming channel to another wavelength at the outgoing channel.
Assume that two packets are destined to go out of the same output port at the same time. Both packets can be still transmitted, but on two different wavelengths.
Different categories of wavelength conversion are:
  Full conversion:
    Convert an incoming wavelength to any outgoing wavelength.
  Limited conversion:
    Convert an incoming wavelength to a subset of the outgoing wavelengths.
  Fixed conversion:
    Convert an incoming wavelength to a fixed outgoing wavelength
  Sparse wavelength conversion:
    Networks are comprised of a mix of wavelength converters.

## Slide 5: Wavelength Continuity Constraint
A light-path that operates on the same wavelength on all fiber links that it traverses.
leads to inefficient utilization of wavelength channels and higher blocking probability.
For example:
  Request rejected even though a route is available but the same wavelength in not, on all the links along the route.
RWA becomes critical in WDM routing networks where goal is to maximize throughput by optimally assigning routes and wavelengths to a given traffic pattern.
If switch equipped with wavelength converter, no wavelength continuity constraint

## Slide 6: Routing and Wavelength Assignment (RWA)
RWA algorithms based on traffic assumptions:
Static Traffic
  Set of connections for source and destination pairs are given
Dynamic Traffic
  Connection requests arrive to and depart from network one by one in a random manner.
  Performance metrics used fall under one of the following three categories:
    Number of wavelengths required
    Connection blocking probability: Ratio between number of blocked connections and total number of connections arrived
    Fiber cost or number of fiber resources handled at the routing nodes.

## Slide 7: Light Path Establishment Problem
Static Light-path Establishment (SLE ) Problem
  RWA problem for static traffic.
  Two sub-problems: routing and wavelength assignment
    Each NP complete.
  Heuristic wavelength assignment algorithms: Largest-First and Smallest-Last.
Dynamic Light-path Establishment (DLE) Problem
  Assumes a fixed number of wavelengths exist for allocation.
  RWA problem for dynamic traffic.
  Objective: setup light paths and assign wavelengths such that it:
    minimizes amount of connection blocking or
    maximizes number of connections that are established.
  Heuristic wavelength assignment algorithms: Random Assignment, First-Fit, Least-Used, Most-Used, Min-Product, Least-Loaded, Max-Sum, Relative Capacity Loss.

## Slide 8: Static Wavelength Assignment
Light-paths and their routes known in advance
Need to assign wavelength to each light-path, such that light-paths on a given link have different wavelengths.
Can be solved by formulating problem as
  Integer linear program (ILP)
  Graph-coloring problem.
Objective: to assign wavelengths to light-paths that minimizes number of wavelengths used.

## Slide 9: Largest First Algorithm
Label nodes as v1, v2, v3 … vn.
Apply largest first vertex ordering and use node index to break ties.
Vertices V(G)=v1,v2,……..vn ordered
such that deg(vi) >= deg(vi+1)
Node with highest degree is assigned wavelength.
Remove this node from graph and re-order nodes
Repeat process of assigning wavelengths until all nodes are assigned a wavelength.

## Slide 10: Largest First Algorithm
B
A
F
C
D
E
1
4
5
2
3
1 = (A, C)
2 = (A, E)
3 = (F, C)
4 = (B, D)
5 = (B, E)
Light-path Requests

## Slide 11
Largest First Algorithm
4
1
0
1
0
2
3
2
1
5
Building AG
Step 1: 1  2
1  4
Step 2: 2  3
Step 3: 3  5
Step 4: 4  2
Step 5: X
Auxiliary Graph (AG)
Largest First Ordering: < 2, 1, 3, 4, 5>
< 0, 1, 1, 2, 0>
Wavelength Assignment:

## Slide 12: Smallest Last Algorithm
Label nodes as v1, v2, v3,… vn.
Apply smallest last vertex ordering and use node index to break ties.
Vertices V(G)={v1,v2,……..vn} ordered
such that, deg(vi) <= deg(vi+1).
Node with highest degree is assigned a wavelength
Remove this node from graph and re-order nodes
Repeat process of assigning wavelengths until all the nodes are assigned a wavelength

## Slide 13
Smallest Last Algorithm
4
2
1
0
1
0
3
2
1
5
Building AG
Step 1: 1  2
1  4
Step 2: 2  3
Step 3: 3  5
Step 4: 4  2
Auxiliary Graph (AG)
Smallest Last Ordering: < 5, 3, 1, 2, 4 >
< 4, 2, 1, 3, 5 >
< 0, 1, 2, 0, 1 >
Wavelength Assignment:

## Slide 14: Dynamic Wavelength Assignment Problem
First Fit
Longest First
Least Used
Most Used
Min-Product
Least Loaded
Max-Sum
Relative Capacity Loss

## Slide 15: First Fit and Longest First Assignment
First Fit Assignment:
  Wavelengths are numbered and ordered
  When searching for available wavelengths, a lower numbered wavelength is considered before a higher numbered wavelength
  Ensures that wavelength towards lower-end of ordered set of wavelengths are used more
  Advantages
    Low blocking probability
    Fairness during assignment
    Small computational complexity
Longest First Assignment :
  Order the light-path requests based on their length
  Assign the longest light-path first.

## Slide 16
Longest First Wavelength Assignment
[ {1,3}, {1,2} , {4,5} , {3,5} , {2,4} , {3,4} ]
a b c d e f
First-Fit Wavelength Assignment

## Slide 17: Least and Most Used Assignment
Least Used (LU):
  Selects a wavelength that is least used in the network, thereby attempting to balance the load among all the wavelengths.
  Goal of this scheme looks attractive but, its performance is worse of than random assignment.
  Requires additional storage and computation cost.
Most Used (MU):
  Selects the most used wavelength in the network for the next assignment.
  MU packs the connections into fewer wavelengths and conserves the spare capacity.
  MU is outperforms the LU in several aspects.

## Slide 18
Least Used Assignment
Most Used Assignment
[ {1,3}, {1,2} , {4,5} , {3,5} , {2,4} , {3,4} ]
a b c d e f

## Slide 19: Max-Sum
Considers all possible paths in the network and attempts to maximize the remaining path capacities after light path establishment.
Assumes traffic matrix known in advance.
Path capacity on wavelength j, is the number of fibers on which wavelength j is available on the most congested link along the path p.
Path capacity of path p is sum of path capacities on all wavelengths.
Select a wavelength, so that path capacity after light path establishment is maximum.
Once connection has been established network state is updated and the next connection request is handled the same way.

## Slide 20
{(2-4), (1-5), (3-6), (0-3)}
a b c d
Initial wavelength assignment
Max-Sum allocation of (2-4)
  0 1 1
  1 2 0
  1 1 1
(1-5) (3-6) (0-3)
2
3
3

## Slide 21: Max-Sum
To establish (2-4). Other requests: P={(1-5), (3-6), (0-3)}.
If wavelength 0 is assigned to (2-4), then for remaining requests:
  For (1-5), cannot use 0 as it is used by (2-4), cannot use 1 as it is used by (0-3). We have just only one, 2.
  For (3-6), can use wavelengths 1 and 2. We have two options.
  For (0-3), cannot use any of the available ’s. We have no option.
Adding up all these options
  For 0, C1 = 1 + 2 + 0 = 3
  For 1, C2 = 1 + 1 + 1 = 3
  For 2, C3 = 0 + 1 + 1 = 2
Choose 0

## Slide 22: Relative Capacity Loss (RCL)
Minimizing total capacity loss sometimes doesn’t lead to the best choice of wavelength.
RCL calculates relative capacity loss for each path on each available wavelength and then chooses the wavelength that minimizes sum of the relative capacity loss on all the paths.
Let R( (j),p) = Options before wavelength assignment
R(’(j),p) = Options after wavelength assignment
R( (j),p) - R(’(j),p)
R( (j),p)
Calculate, Total RCL for each wavelength for each light-path.
Select wavelength with minimum Total RCL.
RCLj =

## Slide 23
{(2-4), (1-5), (3-6), (0-3)}
a b c d
Initial wavelength assignment
RCL allocation of (2-4)
  (1-0)/1 (2-1)/2 (1-1)/1
(1-5) (3-6) (0-3)
RCL3 = 1.5
RCL2 = 0.5
RCL1 = 1.0
  (1-1)/1 (2-1)/2 (1-1)/1
  (1-1)/1 (2-2)/2 (1-0)/1

## Slide 24: Relative Capacity Loss
Before Assignment
Light-path Uses R( (j),p)
(1-5) 2 1
(3-6) 1, 2 2
(0-3) 0 1
Assigning (2,4), (1-5) (3-6) (0-3)
For 0, RCL 1 = (1-1)/1 + (2-2)/2 + (1-0)/1 = 1.0
For 1, RCL 2 = (1-1)/1 + (2-1)/2 + (1-1)/1 = 0.5
For 2, RCL 3 = (1-0)/1 + (2-1)/2 + (1-1)/1 = 1.5
Choose 1, yields minimum RCL.

## Slide 25: Min-Product Algorithm
Designed for multi-fiber networks
Minimize the number of fibers being used at a time
Suppose, we are required to assign a wavelength for a particular connection request
We consider each available wavelength and compute the number of fibers carrying the same wavelength on each link in the light-path
For each wavelength, the number of fibers on each link are all multiplied together
Allocate that wavelength to connection request which minimizes this value, across all available wavelengths

## Slide 26: Min-Product Algorithm
For each wavelength, compute the product:
        w1, 2*3*1*3*5 =90
        w2, 3*2*4*1*2 = 48
        w3, 1*2*1*2*1 = 4

## Slide 27: Least Loaded
Designed for multi-fiber networks.
Select wavelength with the largest residual capacity for the most loaded link along the route p (of the connection request).
Select the minimum indexed wavelength j among the set of wavelengths available Sp, so that it achieves
        jSp
      Max{ min(Ml-Dlj) }
      lП(p)
      Ml = maximum number of fiber/link

## Slide 28: Least Loaded
Consider the same example.
The residual capacities corresponding to each of the wavelengths in each of the links are in brackets .
Assume maximum number of fibers per link is the same for all links and is 7.

## Slide 29: Least Loaded
Setting up connection from Link 1 and Link 2.
  Wavelength 1,
    residual capacities along Link1 + Link 2 are 5,4. Minimum is 4.
  Wavelength 2,
    residual capacities along Link1 + Link 2 are 4,5. Minimum is 4.
  Wavelength 3,
    residual capacities along Link1 + Link 2 are 6,5. Minimum is 5.
We choose wavelength that maximizes value of minimum individual residual capacities.
It is wavelength 3.

## Slide 30: Conclusion and Future Work
What is a light-path?
Static and Dynamic Traffic
Static and Dynamic Light-path Assignment
Examples of each heuristic algorithms
Distributed RCL Techniques
Wavelength Conversion Techniques and minimization of Wavelength Converters.

## Slide 31: References
Hui Zang, Jason P. Jue and Biswanath Mukherjee, “A Review of Routing and Wavelength Assignment Approaches for Wavelength-Routed Optical Networks,”.
B. Mukherjee, “Optical Communication Networks,” McGraw-Hill, New York, 1997.
S. Subramanian and R.A. Barry, “Wavelength Assignment in Fixed Routing WDM Networks,” IEEE International Conference on , Volume: 1 , pg. 406 -410 vol.1 1997.